## Slide 1: PLC Programming Part 1
Problems with large programs and solution

## Slide 2: PLC Programming
Problems with writing PLC Code for Large program
  Cumbersome
  Time-Consuming and difficult to develop, debug and maintain
  Slow down the scan time
  Hard to follow for others

## Slide 3: PLC Programming
Solving the problem with writing big programs
  Use programming paradigm
    Structured programming is a programming paradigm aimed at improving the clarity, quality, and development time of a computer program by making extensive use of the structured control flow constructs of selection (if/then/else) and repetition (while and for), block structures, and subroutines in contrast to using simple tests and jumps such as the go to statement, which can lead to “spaghetti code” that is potentially difficult to follow and maintain.
    https://press.rebus.community/programmingfundamentals/chapter/structured-programming/
  Develop a framework
    Descries a set of solutions and processes to aid in the development of software
    Benefits
      Saves time
      Ensure best practices are followed

## Slide 4: PLC Programming
Control Structures
  The mechanisms that allow us to control the flow of execution are called .
    Sequence
      Do one instruction then the next and the next.
      Just do them in a given sequence or in the order listed
    Selection
      Choose between two or more flows.
    Iteration, Repetition or Looping
      Allows code to be executed several times until some condition has been met
https://press.rebus.community/programmingfundamentals/chapter/structured-programming/

## Slide 5: Intro to PLC Programming
Defining a Control Structure
  That can run a sequence in a controlled fashion
    Numerically Sequenced
      To easily follow the path of execution
  Can be skipped to improve cycle time
    Use jump and label in a limit fashion
    Stage and End Stage command
    Controlled by an enable flag (bit)
  Enter or start the Control Structure
    Start process flag
  Exit or stop the Control Structure
    Stop process flag
    Stop and cleans up the Control Structure process

## Slide 6: Intro to PLC Programming
Defining a Block of code for Omron CX-Programmer

## Slide 7: Intro to PLC Programming
Defining a Block of code for Omron SYSMAC

## Slide 8: Intro to PLC Programming
Defining a Block of code for Omron SYSMAC

## Slide 9: Intro to PLC Programming
Defining a Block of code for Kollmorgen Automation Suite
LeftFoilOn[x] is an array of 16 bool
LeftFoilOn[0] is the Enabling bit
If LeftFoilOn[0] is Off the
  -->> LeftFoilAitOn_End is the Jump Statement that bypasses this Network of code.
  On Network #2: LeftFoilAirOn_End is the label that the Jump statement refers to.
The Reset16BitArray function block is used to reset the individual bits in the array
LeftFoilOn[1] is the starting bit for the block of code
LeftFoilOn[1] rung sets an output variable “Outputs_LeftFoilPlattenAir” then proceed to reset the current rung LeftFoilOn[1] then set the next rung LeftFoilOn[2].

## Slide 10: Intro to PLC Programming
Defining a Block of code for Kollmorgen Automation Suite : Continued
LeftFoilAirOn[2] Rung enables a Timer On function block defined by literal time variable time#10ms.
After 10ms the LeftFoilAirOn[2] rung is Reset and the Last Bit in the array is set to finish the block.
LeftFoilAirOn[15] activates the Reset16BitArray function block which reset the array of bits in the LeftFoilAirOn array thereby turning off the block of code.
This block code represents the basic building block of ladder logic that will be used to write your programs.