## Slide 1: Introduction To PLC Programming

## Slide 2: Intro to PLC Programming
For most PLC, the programming languages is based on the IEC 61131-3
  Ladder diagram (LD), graphical
  Function block diagram (FBD), graphical
  Structured text (ST), textual
  Instruction list (IL), textual
  Sequential function chart (SFC), graphical
Two types of PLC
  Address Based
  Variable Based

## Slide 3: Intro to PLC Programming
Basic Data Types
  Boolean (1 bit)
  WORD (16 bits), DWORD (32 bits)
    does not represent a number only an array of bits
    Most PLC allows you to access these bits using the Dot Operator or [].
  INT (16 bits) – represent a signed number 0 – 65535
  UINT (16 bits) – represent a unsigned number - 0 to 65535
  DINT (32 bits) – represent a signed number (-2147483648) – (2147483648)
  UDINT (32 bits) - represent a unsigned number
  REAL (32 bits) – single precision floating point number (IEEE-754 )
  LREAL (64 bits) –double precision floating point number (IEEE-754 )
  Time (64 bits) – define a time variable (HH:MM:SS:MS:US:NS)
  String ( 8 bits * Char) – defines an array of chars

## Slide 4: Intro to PLC Programming
Array
  collection of data elements of the same data type
Structure
  Allows of a set of variables to be grouped together
Unions
  data structure that usually contains different data types
  All components have the same offset
  occupy the same memory space
Enumeration
  An ordered list of all items in a collection

## Slide 5: Intro to PLC Programming
Basic Ladder Elements
  Open Contact
  Close Contact
  Coil
  Set
  Reset

## Slide 6: Intro to PLC Programming
Write a basic Ladder diagram

## Slide 7: Intro to PLC Programming
Problems with writing PLC Code for Large program
  Cumbersome
  Difficult to debug
  Slow
  Hard to follow

## Slide 8: Intro to PLC Programming
Solving the problem with writing big program
  Structured programming is a programming paradigm aimed at improving the clarity, quality, and development time of a computer program by making extensive use of the structured control flow constructs of selection (if/then/else) and repetition (while and for), block structures, and subroutines in contrast to using simple tests and jumps such as the go to statement, which can lead to “spaghetti code” that is potentially difficult to follow and maintain.
https://press.rebus.community/programmingfundamentals/chapter/structured-programming/

## Slide 9: Intro to PLC Programming
    Solving the problem with writing big program
The mechanisms that allow us to control the flow of execution are called control structures.
  Sequence – Very boring. Simply do one instruction then the next and the next. Just do them in a given sequence or in the order listed. Most lines of code are this.
  Selection – This is where you select or choose between two or more flows. The choice is decided by asking some sort of question. The answer determines the path (or which lines of code) will be executed.
  Iteration – Also known as repetition, it allows some code (one to many lines) to be executed (or repeated) several times. The code might not be executed at all (repeat it zero times), executed a fixed number of times or executed indefinitely until some condition has been met. Also known as looping because the flowcharting shows the flow looping back to repeat the task
https://press.rebus.community/programmingfundamentals/chapter/structured-programming/

## Slide 10: Intro to PLC Programming
Define a Block of code
  That can run a sequence in a controlled way
    Numerically Sequenced
  can be skipped to improve cycle time
    Use jump and label in a limit fashion
    Stage and End Stage command
  Have enable flag (bit)
  Enter or start the sequence
  Exit or stop the sequence

## Slide 11: Intro to PLC Programming
Defining a Block of code for Omron CX-Programmer

## Slide 12: Intro to PLC Programming
Defining a Block of code for Omron SYSMAC

## Slide 13: Intro to PLC Programming
Defining a Block of code for Kollmorgen Automation Suite
LeftFoilOn[x] is an array of 16 bool
LeftFoilOn[0] is the Enabling bit
If LeftFoilOn[0] is Off the
  -->> LeftFoilAitOn_End is the Jump Statement that bypasses this Network of code.
  On Network #2: LeftFoilAirOn_End is the label that the Jump statement refers to.
The Reset16BitArray function block is used to reset the individual bits in the array
LeftFoilOn[1] is the starting bit for the block of code
LeftFoilOn[1] rung sets an output variable “Outputs_LeftFoilPlattenAir” then proceed to reset the current rung LeftFoilOn[1] then set the next rung LeftFoilOn[2].

## Slide 14: Intro to PLC Programming
Defining a Block of code for Kollmorgen Automation Suite : Continued
LeftFoilAirOn[2] Rung enables a Timer On function block defined by literal time variable time#10ms.
After 10ms the LeftFoilAirOn[2] rung is Reset and the Last Bit in the array is set to finish the block.
LeftFoilAirOn[15] activates the Reset16BitArray function block which reset the array of bits in the LeftFoilAirOn array thereby turning off the block of code.
This block code represents the basic building block of ladder logic that will be used to write your programs.