## Slide 1: Introduction To PLC

## Slide 2: What Is an PLC ?
PLC or Programmable Logic Controller
These are industrial micro controllers that are design to control automated process from machine to whole factories.
These controller’s run RTOS(Real Time Operating System)
  Deterministic (predictable execution pattern)
  Deadline (response within determine time frame

## Slide 3: History of PLC
The First PLC called to Modicon (modular digital controller) 081
Design by company called Bedford Associates in 1969.
Allen Bradley also design during this time.

## Slide 4: PLC Hardware
Digital Inputs
  High Speed For Encoder
  Interrupts
  Regular Inputs
Analog Input
  0 – 10v , 0- 20mA
Digital Outputs
  High Speed For Stepper Motor
  Pulse Width Modulation
  Regular Output
Analog Output
  0 – 10v , 0- 20mA

## Slide 5: PLC Hardware
Open Systems Interconnection (OSI) model
  Comprise of 7 layers
    Physical Layer
      Contain the infrastructure that makes communication on networks possible.
      So defines the electrical, mechanical, procedural, and functional specifications for activating, maintaining, and deactivating physical links between network devices
    Data Link Layer
    Network Layer
    Transport Layer
    Session Layer
    Presentation Layer
    Application Layer

## Slide 6: PLC Hardware
Fieldbus
  Vendor Specific communication Protocols
    FINS
  Industrial Standard Communication
    EtherCAT
    Ethernet/IP (CIPS)
    Serial Port
    Ethernet
    OPC-UA

## Slide 7: Intro to PLC Programming
For most PLC, the programming languages is based on the IEC 61131-3
  Ladder diagram (LD), graphical
  Function block diagram (FBD), graphical
  Structured text (ST), textual
  Instruction list (IL), textual
  Sequential function chart (SFC), graphical
Two types of PLC
  Address Based
  Variable Based